## Slide 1
Burn Cut Blast Design
& Performance Analysis
Underground blast design in AutoCAD with Excel calculations and safety checks
Prepared by
Lakshay Soni
Project: Burn cut design with AutoCAD drawings, Excel calculations, and fragmentation, vibration and sensitivity analysis
This deck includes definitions, formulas, calculation tables, AutoCAD screenshots, and blast performance and safety analysis.
Burn Cut in Underground Blasting
Slide 1

## Slide 2
Project Overview
What the presentation covers
Burn Cut in Underground Blasting
Main idea
Burn cut is a parallel-hole blasting pattern used in underground excavation. It creates an initial cavity in the rock face so the remaining holes can break rock efficiently. The design process in this project uses AutoCAD for geometry and Excel for charge and burden calculations.
Why this method?
Good for hard rock excavation
Improves fragmentation and advance
Works with a single free face
Useful for tunnels and drifts
What is included in this deck?
Definitions and cut types
AutoCAD top, side and front views
Excel inputs, formulas and output tables
Blast performance and safety analysis
Slide 2

## Slide 3
Burn Cut: Definition
A core concept in underground drilling and blasting
Burn Cut in Underground Blasting
Definition
Burn cut is a drilling pattern in which one or more empty holes are placed near the center of the face and the surrounding charged holes are drilled parallel to them. The empty holes act as a relief space so the rock can break towards the cavity created by the first blast.
Key points
Parallel holes are used instead of angled holes.
The cut creates the first free face inside the face.
It is especially useful in hard rock.
Important terms
Empty hole
A hole with no explosive to create space
Charge hole
Hole loaded with explosive
Burden
Distance from hole to free face
Stemming
Inert material at the top of a hole
Relief
Void that helps rock breakage
Slide 3

## Slide 4
Burn Cut Design Basics
How the pattern is formed in the face
Burn Cut in Underground Blasting
Geometry of a burn cut
The central empty holes create the cavity. The surrounding holes are fired in sequence so the broken rock moves into the void.
Empty holes
Charged holes
Design constraints
Single free face
Rock type and strength
Hole diameter and depth
Explosive type and load
Sequence of firing
Common hole groups
Cut holes or cut spreader holes
Stoping holes around the cut
Wall, roof and floor holes
Lifters near the floor
Slide 4

## Slide 5
AutoCAD Views Created
Top view, side view and front view of the burn cut pattern
Burn Cut in Underground Blasting
Top view
Top view
Side view
Side view
Front view
Front view
Each view helps verify spacing, alignment, depth and the position of the cut holes.
Slide 5

## Slide 6
Front View
Full face arrangement of holes in the burn cut pattern
Burn Cut in Underground Blasting
Front view screenshot
Use this view to show the symmetry of the hole pattern and the curved boundary of the face.
Slide 6

## Slide 7
Side View
Hole inclination and level arrangement
Burn Cut in Underground Blasting
Side view screenshot
This view is useful to explain the depth, parallel alignment and the position of the empty holes.
Slide 7

## Slide 8
Top View
Plan view of the burn cut layout
Burn Cut in Underground Blasting
Top view screenshot
This view helps in checking spacing, row pattern and the relationship between cut holes and stoping holes.
Slide 8

## Slide 9
Excel Inputs and Formulas
The main values used in the burn cut calculation sheet
Burn Cut in Underground Blasting
Input values from Excel
Diameter of empty holes (De)
102 mm
Length of holes (L)
3 m
Charge hole diameter (d)
45 mm
Rock constant (C)
0.6
Explosive density
0.85 g/cm³
RWS
1
Formulas used
Stemming length
T = 10 × d
Charge length
Lc = L - T
Charge concentration
Q(kg/m) = 7.85 × 10^-4 × d² × density
Burden equation
B = 0.88 × q^0.35
Total powder factor
PF = Q_total / rock volume
Slide 9

## Slide 10
Cut Section Calculations
Worked values from the Excel sheet for the first four sections
Burn Cut in Underground Blasting
Calculated burn cut sections
Section
Burden B (m)
Side A (m)
q (kg/m)
Q = q×4
Q×L
First
0.153
0.216
0.377
1.509
3.847
Second
0.216
0.459
0.356
1.423
3.627
Third
0.459
0.974
0.754
3.018
7.695
Fourth
0.974
2.066
1.600
6.401
16.323
These values match the Excel calculations used to design the burn cut sections.
Slide 10

## Slide 11
Rest Holes and Final Results
Total charge and powder factor from the Excel file
Burn Cut in Underground Blasting
Remaining hole calculations
Q(kg/m)
1.351
Burden B (m)
0.978
Floor holes
12
Wall holes
8
Roof holes
8
Stoping holes
50
Final values from Excel
Cut charge total
31.49 kg
Other holes charge total
60.80 kg
Total charge Q_total
92.30 kg
Rock volume
58.8 m³
Powder factor
1.570 kg/m³
The powder factor gives a quick idea of how much explosive is used per cubic meter of rock.
Slide 11

## Slide 12
Burn Cut in Underground Blasting
Fragmentation Estimate (Kuz-Ram Model)
Predicting the mean rock fragment size produced by the existing blast design
Slide 13
Kuz-Ram formula
X50 = A × (V0/Qe)^0.8 × Qe^(1/6) × (115/RWS)^(19/30)
X50 = mean fragment size (cm)
A = rock factor (blastability index)
V0/Qe = rock volume broken per kg of explosive = 1 / powder factor
Qe = mass of explosive per hole (kg)
RWS = relative weight strength vs. ANFO (%)
Inputs used (from this design)
Rock factor, A (assumed: competent hard rock) | 10
Powder factor (from Excel sheet) | 1.570 kg/m³
V0/Qe = 1 / powder factor | 0.637 m³/kg
Total charge / total holes ≈ Qe (avg. per hole) | 92.30 kg / 94 ≈ 0.98 kg
Relative weight strength, RWS (ANFO-equivalent) | 100%
Estimated mean fragment size: X50 ≈ 7.6 cm
This is a design-stage estimate — A and Qe are assumed/averaged values that would normally be refined against site-specific rock mass data and monitored blast results.

## Slide 13
Burn Cut in Underground Blasting
Design Sensitivity: Burden vs. Hole Diameter
How the allowable burden changes as charge-hole diameter increases
Slide 14
Calculated values
d (mm) | q (kg/m) | B (m)
25 | 0.417 | 0.648
32 | 0.683 | 0.770
38 | 0.964 | 0.869
45 | 1.351 | 0.978
51 | 1.735 | 1.067
64 | 2.734 | 1.251
76 | 3.856 | 1.411
d = 45 mm (highlighted) is the diameter actually used in this design.
Burden vs. hole diameter
0.65
25
0.77
32
0.87
38
0.98
45
1.07
51
1.25
64
1.41
76
Burden B (m)
Hole diameter d (mm)
Larger holes take a proportionally larger charge, which allows a wider burden — this is the design trade-off between hole count, drilling cost and charge per hole.

## Slide 14
Burn Cut in Underground Blasting
Blast Vibration & Safety (PPV Check)
Estimating ground vibration using the USBM scaled-distance approach
Slide 15
Scaled-distance formula
PPV = K × (D / √W)^(-B)
D = distance from the blast (m)
W = max. charge weight per delay (kg) = 6.4 kg here
K, B = site constants (typical USBM values: K = 1140, B = 1.6)
Safe standoff distance for this charge (W = 6.4 kg):
≈ 18 m for a 50 mm/s limit (typical mine structures)
≈ 75 m for a 5 mm/s limit (sensitive/heritage structures)
Predicted PPV vs. distance
Distance D (m) | Predicted PPV (mm/s) | Note
5 | 383 | Exceeds mine-structure limit
10 | 126 | Exceeds mine-structure limit
20 | 42 | Within mine-structure limit
30 | 22 | Within mine-structure limit
50 | 10 | Within mine-structure limit
K and B are standard illustrative USBM values — a real site would calibrate these from monitored test-blast vibration records.

## Slide 15
Burn Cut in Underground Blasting
Initiation Sequence & Timing
Delay sequence that controls how broken rock moves toward the cut
Slide 16
Firing sequence, cut outward to perimeter
Cut
(sections 1-2)
0 ms
Cut
(sections 3-4)
50 ms
Stoping
holes
100 ms
Wall
holes
150 ms
Roof
holes
175 ms
Floor /
lifters
200 ms
Sequence direction → each group is fired after the previous one has had time to move rock into the newly created void.
Why this order: the central cut fires first to create a free face inside the heading; stoping holes then break toward that cavity; perimeter (wall/roof) holes shape the profile; floor lifters fire last to clear the muck fully.

## Slide 16
Burn Cut in Underground Blasting
Cut Pattern Comparison
How burn cut compares with other common parallel and angled cut types
Slide 17
Cut type | Hole arrangement | Best suited to | Key advantage
Burn cut | Parallel holes; empty relief hole(s) at center | Hard, competent rock; small-to-medium drifts | High advance per round; simple parallel drilling
Wedge (V) cut | Angled holes forming a V toward the face | Medium-strength rock; wider tunnels | Works across a range of rock types, no empty holes needed
Fan cut | Angled holes radiating from a central point | Larger cross-sections; weaker rock | Efficient for large openings
Pyramid (diamond) cut | Angled holes converging to one point | Very hard rock; small drifts | Deep, tight cavity; strong initial relief
Why burn cut was chosen here: it works with a single free face and purely parallel drilling — well suited to hard rock drifting, where accurately aligning angled holes (as wedge or fan cuts need) is harder in practice.

## Slide 17
Conclusion
Key takeaways from the design and analysis
Burn Cut in Underground Blasting
Key points
Burn cut is suitable for underground hard-rock blasting.
The empty holes create the initial relief cavity.
AutoCAD helps visualize the hole pattern clearly.
Excel helps calculate burden, charge and powder factor.
Thank you
Lakshay Soni
Slide 17